## Slide 1
SafeCharge:
Interactive BMS Digital Twin
Group 6
Digital Engineering Summer Semester Project
Otto-von-Guericke-University Magdeburg
Sprint 2 — Concept Update & SOH Integration
Document date: 14 May 2026 | Sprint 2 due: 22 May 2026

## Slide 2
Where We Are: Sprint 1 Recap
Concept locked
Interactive 3D digital twin of a Li-ion pack + BMS. Cause-and-effect learning loop: Input → Process → BMS Logic → Visualization → Result.
Architecture defined
BMS block diagram, sensor inputs, electro-thermal coupling. Safety thresholds locked at 45 °C (cooling) and 60 °C (runaway alarm).
Pipeline ready
Unity + GitHub configured. CEE owns process math; DE/DKE owns Unity build, Blender assets, and UI.
Sprint 1 status: all planned deliverables complete. Concept, safety thresholds, Unity + GitHub setup, UI wireframes, and the flow-visualization concept are signed off.
SafeCharge: BMS Digital Twin
2

## Slide 3
Professor's Feedback — Cell Health Matters
The current concept treats State-of-Charge as a single honest number. In reality, the displayed % understates how degraded the pack actually is.
When one or more cells have a lower State-of-Health (SOH), the pack’s usable capacity is limited by the weakest cell. A pack reading 80% SOC may only deliver the energy a healthy pack would deliver at 64%.
What the app must show
Per-cell SOH visible in the cell-level view, not just pack-level SOC.
Difference between displayed SOC and actual usable SOC.
Real-world consequence of that gap: EV driving range that drops as cells degrade.
Sprint 2 response: introduce SOH math + a 4×4 cell-health heatmap + an EV range estimator that exposes the gap.
SafeCharge: BMS Digital Twin
3

## Slide 4
Sprint 2 Objectives
By 22 May 2026 the team will have:
1
Process equations
SOC, Joule heating, and lumped thermal balance documented and parameterised.
2
SOH math (NEW)
Per-cell SOH and weakest-cell-limits-pack rule integrated into the model.
3
EV range estimator (NEW)
Range in km wired to SOH-corrected usable capacity; worked example for result card.
4
Initial 3D assets
Battery pack + 4×4 cell grid + cooling fan authored in Blender, exported as .fbx.
5
Unity scene scaffold
Loads the .fbx, runs §4 equations in FixedUpdate, placeholder SOH-driven shaders.
6
UI dual gauge + heatmap
Dual SOC ring, 16-cell SOH heatmap, range readout in km.
SafeCharge: BMS Digital Twin
4

## Slide 5
Process Equations — SOC & Joule Heating
State of Charge (SOC)
SOC(t) = SOC₀ − (1 / Q_nom) · ∫ I(τ) dτ
Discrete: SOC[k+1] = SOC[k] − (I[k]·Δt) / (3600 · Q_nom)
Coulomb counting. Sign convention: discharge current is positive.
Joule Heating & Lumped Thermal
Q̇_gen = I² · R_int(SOC, T)
m · c_p · dT/dt = Q̇_gen − h · A · (T − T_amb)
c_p = 800 J/(kg·K) h ≈ 10 W/(m²K) passive, ~40 active
Safety thresholds (locked from Sprint 1):
Cooling fan activates at T_pack > 45 °C.
Runaway alarm and BMS current cut at T_pack > 60 °C.
Operating ambient range: −10 °C to +50 °C. Current input: −5C to +5C.
Refs: Plett (2015) BMS Vol. I — Battery Modeling; Bernardi, Pawlikowski & Newman (1985) J. Electrochem. Soc.; Forgez et al. (2010) J. Power Sources.
SafeCharge: BMS Digital Twin
5

## Slide 6
NEW — SOH & Weakest-Cell Math
Each cell j carries an SOH ∈ [0, 1] = current full capacity / nominal. End-of-life at SOH = 0.80 (IEC 62660-1).
Per-cell SOH
SOH_j = Q_full,j / Q_nom
Q_full,j = current full capacity of cell j after ageing
Usable pack capacity (series string of N cells)
Q_pack_usable = minⱼ ( Q_full,j ), j = 1 … N
The worst cell sets the ceiling for the whole pack
Displayed vs Actual SOC
SOC_actual = SOC_displayed · SOH_pack
Example: SOC_displayed = 80 %, SOH_pack = 0.80 → SOC_actual = 64 %
4 × 4 cell heatmap (mockup)
0.93
0.91
0.90
0.88
0.92
0.89
0.87
0.85
0.90
0.86
0.82
0.78
0.88
0.84
0.78
0.72
Weakest cell: 0.72 → pack ceiling
Refs: Dubarry, Vuillaume & Liaw (2009) J. Power Sources; Plett (2004) J. Power Sources; IEC 62660-1:2018.
SafeCharge: BMS Digital Twin
6

## Slide 7
NEW — EV Range Estimator
To translate the SOC/SOH gap into something the user can feel, the dashboard shows remaining range in km.
Usable energy
E_usable (kWh) = V_nom · Q_pack_usable · SOC_displayed / 1000
V_nom = 350 V (demo pack)
Estimated remaining range
Range (km) = E_usable / c_drive
c_drive = 0.18 kWh/km (mid-size EV)
Worked example — demo scenario
Nominal pack: Q_nom = 100 Ah, V_nom = 350 V
Displayed SOC: 80 %
If pack is healthy (SOH = 1.00):
E = 350 · 100 · 0.80 / 1000 = 28.0 kWh
Range ≈ 156 km
If weakest cell SOH = 0.72:
Q_usable = 72 Ah, E = 20.2 kWh
Range ≈ 112 km
Loss the user sees: −44 km on the same 80 % reading.
Refs: Larminie & Lowry (2012) Electric Vehicle Technology Explained; Sweeting et al. (2011) Int. J. Sustainable Engineering.
SafeCharge: BMS Digital Twin
7

## Slide 8
UI Updates — Dual Gauge, Heatmap, Range
Dual SOC Gauge
Outer ring = displayed SOC. Inner ring = SOC_actual. The wedge between them is the SOH penalty the user sees at a glance.
4 × 4 Cell Heatmap
Tile widget mirrors the 3D cell grid. Green → yellow → red colour mapping. Hovering a tile highlights the matching 3D cell.
Range Readout (km)
Two numbers: range if the pack were healthy (grey), range with current SOH (maroon). Delta is the headline number on the result card.
80%
displayed
64% actual
Healthy: 156 km
Actual: 112 km
−44 km lost to SOH
Each UI element binds to a controller script (see next slide for the Unity pipeline).
SafeCharge: BMS Digital Twin
8

## Slide 9
3D & Unity Pipeline
Blender — scripted asset build
Battery pack shell + 4 × 4 cell grid, scripted with bpy.
Each cell named cell_00 … cell_15 — index matches the SOH array in Unity.
Cooling fan unit (housing + 5-blade rotor, separated for spin animation).
Cell cross-section asset, ready for ion-flow particles in Sprint 4.
Headless export — no GUI interaction needed:
blender --background --python build_pack.py -- --rows 4 --cols 4 --out pack.fbx
.fbx with applied transforms, Z-up, 1 unit = 1 m.
Unity — scene scaffold + scripts
BatteryPackController.cs — owns SOC, SOH and thermal state; runs §4 equations in FixedUpdate.
CellGrid.cs — 16-cell array; drives per-cell colour on 3D mesh + heatmap tile.
RangeEstimator.cs — pure function; writes Range_healthy / Range_actual to UI.
BMSLogic.cs — threshold checks (45 °C cooling, 60 °C alarm); raises UI events.
DashboardUI.cs — Unity UI binding; subscribes to controller events.
All five wired behind an interface so Sprint 4 can swap the lumped thermal model for per-cell coupling without breaking UI.
SafeCharge: BMS Digital Twin
9

## Slide 10
Sprint 2 — Task Assignment
Owner | Discipline | Sprint 2 task | Due
Rishi Chalamalasetty | CEE | SOC + Joule heating equations finalised; R_int lookup populated; pack/V_nom defaults agreed. | 16 May
Avinash Lobo | CEE | SOH math + EV range estimator; produce worked-example numbers for the result card. | 16 May
Jashkumar Dhameliya | DE | Blender script (build_pack.py): pack shell + 4×4 grid + fan; .fbx export verified in Unity. | 18 May
Shashi Kumar | DE | Unity scaffold: scene, BatteryPackController, BMSLogic, FixedUpdate loop wired to §4 equations. | 20 May
Anant Sharma | DKE | CellGrid + RangeEstimator; SOH heatmap UI widget; parameter-to-UI mapping validated in-engine. | 20 May
Hari Charan | DE | DashboardUI: dual SOC gauge, range readout, warning banners; integration test. | 21 May
Internal due dates leave 22 May for joint dry-run and slide preparation.
SafeCharge: BMS Digital Twin
10

## Slide 11
Timeline Ahead & Risks
Project timeline
Sprint 1
08 May
Sprint 2
22 May
Sprint 4
19 Jun
Sprint 6
17 Jul
Sprint 8
14 Aug
Final
11 Sep
Key risks for Sprint 2
Risk | Lik. | Impact | Mitigation
Blender .fbx import breaks naming/scale in Unity | Med | High | Scripted export with applied transforms; smoke-test import day one.
R_int lookup data unavailable in time | Med | Med | Default 30 mΩ; flag values as 'placeholder' in the UI.
SOH demo numbers feel arbitrary | Low | Med | Anchor to cited EV consumption; show source on result card.
URP shader compile errors across machines | Med | Med | Pin URP version in manifest.json; commit cache exclusions.
SafeCharge: BMS Digital Twin
11

## Slide 12
References
All formulas in this deck come from published, citable sources:
SOC coulomb counting
Plett, G. L. (2015). Battery Management Systems, Volume I: Battery Modeling. Artech House.
Battery thermal energy balance (Joule heating)
Bernardi, D., Pawlikowski, E., & Newman, J. (1985). A general energy balance for battery systems. J. Electrochem. Soc., 132(1), 5–12.
Lumped cell thermal model
Forgez, C., Do, D. V., Friedrich, G., Morcrette, M., & Delacourt, C. (2010). Thermal modeling of a cylindrical LiFePO₄/graphite lithium-ion battery. J. Power Sources, 195(9), 2961–2968.
Weakest-cell-limits-pack rule
Dubarry, M., Vuillaume, N., & Liaw, B. Y. (2009). From single cell model to battery pack simulation for Li-ion batteries. J. Power Sources, 186(2), 500–507.
SOH estimation framework
Plett, G. L. (2004). Extended Kalman filtering for BMS, Part 3: State and parameter estimation. J. Power Sources, 134(2), 277–292.
80% End-of-Life convention
IEC 62660-1:2018 — Secondary lithium-ion cells for the propulsion of electric road vehicles.
EV range / consumption methodology
Larminie, J., & Lowry, J. (2012). Electric Vehicle Technology Explained (2nd ed.). Wiley.
EV energy-consumption ranges
Sweeting, W. J., Hutchinson, A. R., & Savage, S. D. (2011). Factors affecting EV energy consumption. Int. J. Sustainable Engineering, 4(3), 192–201.
Thermal runaway threshold (≈60 °C)
Wang, Q. et al. (2012). Thermal runaway caused fire and explosion of lithium ion battery. J. Power Sources, 208, 210–224.
Numerical defaults (30 mΩ, 350 V, 0.18 kWh/km, 800 J/(kg·K)) are representative values consistent with Plett (2015) and Larminie & Lowry (2012).
SafeCharge: BMS Digital Twin
12

## Slide 13
Thank You
We are open for questions.
Group 6 · Sprint 2 · May 2026